## Slide 1: Some common networking devices.
Network Interface Card (NIC)
NIC stands on first place. Without this device, networking cannot be done. This is also known as network adapter card, Ethernet Card and LAN card. NIC allows our PC to communicate with other PCs. Basically it converts data transmission technology. A PC uses parallel data transmission technology to transmit data between its internal parts while the media that connects this PC with other PCs uses serial data transmission technology. A NIC converts parallel data stream into serial data stream and vice versa serial data stream is get converted in parallel data stream.

## Slide 2: Types of NICs
There are two types of NICs
Media Specific :- Different types of NICs are required to connect with different types of media. For example we cannot connect wired media with wireless NIC card. Just like this, we cannot connect coaxial cable with Ethernet LAN card.
Network Design Specific :- A specific network design needs a specific LAN card. For example FDDI, Token Ring and Ethernet have their own distinctive type of NICs card. They cannot use other’s NIC card.

## Slide 3: HUB
HUB is used to connect multiple computers in a single workgroup LAN network. Typically HUBs are available with 4, 8,12, 24, 48 ports. Based on port type, there are two types of HUB:-
Ethernet HUB :- In this type of HUB all ports have RJ-45 connectors.
Combo HUB :- In this type of HUB ports have several different types of connectors such RJ-45, BNC, and AUI.
HUBs generally have LED (light-emitting diode) indicator lights on each port to indicate the status of link, collisions, and other information.
There are two types of HUB
Passive HUB:- It forwards the data signal from all ports except the port on which signal arrived. It doesn’t interfere in data signal.
Active HUB:- It also forwards the data signal from all ports except the port on which signal arrived. But before forwarding, it improves quality of data signal by amplifying it. Due to this added features active HUB is also known as repeaters.

## Slide 4: BRIDGE
To improve the performance, usually networks are divided in smaller segments. Bridge is used to divide a large network in smaller segments.
Basic function of Bridge are A) Break a large network in smaller segments.
(B)Join different media types such as UTP with fiber optic and ( C ) Join different network architectures such as Ethernet with Token Ring.
A bridge can connect two different types of media or network architecture but it cannot connect two different types of network layer protocol such as TCP/IP or IPX. Bridge requires same network layer protocol in all segments.
There are three types of bridge:-
Local Bridge :- This bridge connects two LAN segments directly. In Ethernet Implementation it is known as Transparent bridge. In Token Ring network it is called Source-Routed bridge.
Remote Bridge :- This bridge connects with another bridge over the WAN link.
Wireless Bridge :- This bridge connects with another bridge without wiring between them.

## Slide 5: SWITCH
Just like Hub and Bridge, switch is also used to connect multiple computers together in a LAN segment. Switches available with 4,8,12,24,48,64 ports. Each switch port has a separate collision domain. Switch works at layer two in OSI Layer model. At layer two data signals are formatted in frames.
All valid frames are processed and forwarded to their destination MAC address.
Switch makes their switching decisions in hardware by using application specific integrated circuits (ASICs).

## Slide 6: MODEM and Connection Lines
In simple language modem is a device that is used to connect with internet. Technically it is a device which enables digital data transmission to be transmitted over telecommunication lines.
Analog connection line
An existing telephone or cable TV network line that uses analog signals (sound waves) for transportation. Instead of supporting Internet, these lines were primarily installed for their respective requirements.
Digital connection Line
A separate connection line between DTE and DCE. Since it is installed primarily for internet, it uses digital signals for data transportation.
For Analog connection line we have to use Analog modem and for digital line we need to use Digital modem.

## Slide 7: Modem and others
Analog Modem
Analog modem converts Analog signal in digital signal and vice versa.
There are two types of Analog modem; internal and external.
Internal Modem
Internal modem is available as interface card for desktop and as PCMCIA card for laptop.
External Modem
External modem is a separate device that has its own CPU and memory.
Digital Modem
Instead of signal conversion, digital modem performs modulation known as line coding. Line coding is used to modulate the digital signal in such a way that they can be transmitted over the digital line. DSL, ADSL and ISDN modem are the examples of digital modem

## Slide 8: Router
Router is a layer three device which forwards data packet from one logical network segment to another. Router forwards packets on the bases of their destination address. These records are maintained in a database table known as routing table. Routing table can be built statically or dynamically.
Basically routers are used :-
To connect different network segments.
To connect different network protocols such as IP and IPX.
To connect several smaller networks into a large network (known as internetwork)
To break a large network in smaller networks (Known as subnet usually created to improve the performance or manageability)
To connect two different media types such as UTP and fiber optical.
To connect two different network architectures such as token ring and Ethernet.
To connect LAN network with Telco company’s office (Known as DTE device).
To access DSL services (known as DSL Router).

## Slide 9: Brouter
Brouters are the combination of router and bridge.

## Slide 10: Gateway
Gateway is used to forward the packets which are intended for remote network from local network. A default gateway address is the address of gateway device. If packet does not find its destination address in local network then it would take the help of gateway device to find the destination address in remote network. A gateway device knows the path of remote destination address
Examples of Gateway
Email Gateway :- Translate SMTP e-mail in standard X.400 format before forwarding.
GSNW Gateway :- Allow windows clients to access resources from NetWare server.
PAD Gateway :- Provides connectivity between LAN network and X.25 network.

## Slide 11: Proxy
Proxy can be a dedicate device or software. Proxy is used to hide the internal network from external world. All communication will go through the proxy. External computer will be able to access only proxy. Thus Proxy makes tampering with an internal system from the external network more difficult.

## Slide 12: THANK YOU