## Slide 1: COMPUTER NETWORKING
Networking is nothing but a process of connecting two or more computers for sharing file, documents, email and resources such as printer, internet and disk storage.
Networking has single purpose and that is sharing. Computer networking is not a new concept. It has used to look like abacuses. At that time networking was used to share abacus answer with others. Over the time abacuses became computers and networking became more sophisticated. To achieve this goal networks now we use electrical cables, fibre optic cables, and wireless radio signals.

## Slide 2: COMPUTER NETWORKING CONTD……
A complex network may have thousands of computers connected via different communication links. For example Internet that is the largest computer network ever created by mankind.
Internet interconnects thousands of millions of computing devices including PCs, Laptops, Workstations, Server, Smartphones, tablets, TVs, Webcams, Environmental devices. In Networking all these devices are known as Hosts or End system or End devices.

## Slide 3: COMPUTER NETWORKING CONTD
Computer networks use communication links to connection end devices with each other's. When a computer has data for another computer in network it initiates a session for transmission. During this process both computers finalized the rules of transmission such as speed of transmission, size of data file, security measurement of transmission, flow control etc.

## Slide 4: PROTOCOLS
The rules and regulations to transmit data. Protocols control the entire data transmission through the network. Protocols are defined in various network models such as TCP/IP Layer model, OSI Layer model.
During the data transmission sender computer break the data file in small pieces. These pieces are called segment. Each segment properly wrapped with network information. Resulting segments are known as packets.
Packets are sent to the destination computer through the network, where they are reassembled into the original data.

## Slide 5: Requirement of Networking
Every network requires specialized hardware and software to make them work. Following are the essential components for network:
Client computers
End devices that users use to access the shared resources. Usually they run desktop version of OS such as Window 10, Window 7, and Window XP. Client computers are also known as workstations.
Server computers
Computers that provide shared resources. Usually they run sever version of OS such as Window Server 8 or 2003, Linux and NetWare. Server computers run many specialized services to control the shared resources.

## Slide 6: Network interface card
NIC is an interface that enables the computer to communicate over the network. Every computer must have a NIC in order to connect with the network. In earlier time it was a separate card and need to be installed on motherboard. All modern computers have it as the integral part of motherboard.

## Slide 7: Communication links
Communication links are physical media. Every computer network needs some sort of media to transmit the data.
Switches
The media to connect more than two computers in network, we cannot connect them directly. We need a mediator device that allows us to connect all computers together. Switches do this job happily. Each switch contains a certain number of ports. We can use an eight port switch to connect eight computers.
Routers
Router is an intermediate device that speaks all language of network. It makes communication between two different networks.

## Slide 8: Benefits of Networking
Networking is all about sharing. Networking allows us to share three main things: information, resources and applications.
Information sharing
Networking makes it easy to share the information across the network. We can send or receive data files from other computers. We can communicate with each other in network via messaging application for example email service, chat service etc. We can store data in a centralized sever for easy management.

## Slide 9: Resources Sharing
Certain computer resources can be shared in the network such as hard disk, printer, scanner, modem etc. This allows us to track down the uses of resources. For example a network administrator can setup a printer server and share it in network. Then user can use printer server for printing. Now administrator needs only to monitor the print server instead of individual workstations.

## Slide 10: Application sharing
Application sharing is the most common in companies. Companies may have business application that needs to be update by several users. Sharing make it possible. It allows several users to work together on a single application.
Workgroup and Home group both terms are used to define a group of computers those are set to share the resources. Workgroup and Home group both terms are used synonymously in networking but they have some differences based on how computers and other resources are managed in the group.

## Slide 11: Difference between Workgroup and Home GroupWorkgroup
In workgroup all computers have equal rights.
Workgroup cannot be password protected.
Workgroup has a limit of twenty computers.
In workgroup all computers must be on same local network.
Workgroup works on all windows version.
Workgroup works on both IP versions: IPv4 and IPv6.
In workgroup every computer requires same workgroup name.
Workgroup needs technical knowledge to setup.
Workgroup requires security and sharing permissions to be set.
To use a workgroup computer you need to have a user account on that computer.

## Slide 12: Home group
Home group does not have a limit of computers.
You can join as much computers as you want.
Home group can be password protected.
Home group is easy to setup. All sharing options are enabled automatically.
Home group requires IPv6 to work.
Home group can be span over the subnet.
Home group requires window7 or higher version.
A computer network is basically a group of multiple networking devices connected together for data sharing. Collectively networking devices have single purpose “securely transfer data as fast as they can”.

## Slide 13: Some common networking devices.
Network Interface Card (NIC)
NIC stands on first place. Without this device, networking cannot be done. This is also known as network adapter card, Ethernet Card and LAN card. NIC allows our PC to communicate with other PCs. Basically it converts data transmission technology. A PC uses parallel data transmission technology to transmit data between its internal parts while the media that connects this PC with other PCs uses serial data transmission technology. A NIC converts parallel data stream into serial data stream and vice versa serial data stream is get converted in parallel data stream.

## Slide 14: Types of NICs
There are two types of NICs
Media Specific :- Different types of NICs are required to connect with different types of media. For example we cannot connect wired media with wireless NIC card. Just like this, we cannot connect coaxial cable with Ethernet LAN card.
Network Design Specific :- A specific network design needs a specific LAN card. For example FDDI, Token Ring and Ethernet have their own distinctive type of NICs card. They cannot use other’s NIC card.

## Slide 15: HUB
HUB is used to connect multiple computers in a single workgroup LAN network. Typically HUBs are available with 4, 8,12, 24, 48 ports. Based on port type, there are two types of HUB:-
Ethernet HUB :- In this type of HUB all ports have RJ-45 connectors.
Combo HUB :- In this type of HUB ports have several different types of connectors such RJ-45, BNC, and AUI.
HUBs generally have LED (light-emitting diode) indicator lights on each port to indicate the status of link, collisions, and other information.
There are two types of HUB
Passive HUB:- It forwards the data signal from all ports except the port on which signal arrived. It doesn’t interfere in data signal.
Active HUB:- It also forwards the data signal from all ports except the port on which signal arrived. But before forwarding, it improves quality of data signal by amplifying it. Due to this added features active HUB is also known as repeaters.

## Slide 16: BRIDGE
To improve the performance, usually networks are divided in smaller segments. Bridge is used to divide a large network in smaller segments.
Basic function of Bridge are A) Break a large network in smaller segments.
(B)Join different media types such as UTP with fiber optic and ( C ) Join different network architectures such as Ethernet with Token Ring.
A bridge can connect two different types of media or network architecture but it cannot connect two different types of network layer protocol such as TCP/IP or IPX. Bridge requires same network layer protocol in all segments.
There are three types of bridge:-
Local Bridge :- This bridge connects two LAN segments directly. In Ethernet Implementation it is known as Transparent bridge. In Token Ring network it is called Source-Routed bridge.
Remote Bridge :- This bridge connects with another bridge over the WAN link.
Wireless Bridge :- This bridge connects with another bridge without wiring between them.

## Slide 17: SWITCH
Just like Hub and Bridge, switch is also used to connect multiple computers together in a LAN segment. Switches available with 4,8,12,24,48,64 ports. Each switch port has a separate collision domain. Switch works at layer two in OSI Layer model. At layer two data signals are formatted in frames.
All valid frames are processed and forwarded to their destination MAC address.
Switch makes their switching decisions in hardware by using application specific integrated circuits (ASICs).

## Slide 18: MODEM and Connection Lines
In simple language modem is a device that is used to connect with internet. Technically it is a device which enables digital data transmission to be transmitted over telecommunication lines.
Analog connection line
An existing telephone or cable TV network line that uses analog signals (sound waves) for transportation. Instead of supporting Internet, these lines were primarily installed for their respective requirements.
Digital connection Line
A separate connection line between DTE and DCE. Since it is installed primarily for internet, it uses digital signals for data transportation.
For Analog connection line we have to use Analog modem and for digital line we need to use Digital modem.

## Slide 19: Modem and others
Analog Modem
Analog modem converts Analog signal in digital signal and vice versa.
There are two types of Analog modem; internal and external.
Internal Modem
Internal modem is available as interface card for desktop and as PCMCIA card for laptop.
External Modem
External modem is a separate device that has its own CPU and memory.
Digital Modem
Instead of signal conversion, digital modem performs modulation known as line coding. Line coding is used to modulate the digital signal in such a way that they can be transmitted over the digital line. DSL, ADSL and ISDN modem are the examples of digital modem

## Slide 20: Router
Router is a layer three device which forwards data packet from one logical network segment to another. Router forwards packets on the bases of their destination address. These records are maintained in a database table known as routing table. Routing table can be built statically or dynamically.
Basically routers are used :-
To connect different network segments.
To connect different network protocols such as IP and IPX.
To connect several smaller networks into a large network (known as internetwork)
To break a large network in smaller networks (Known as subnet usually created to improve the performance or manageability)
To connect two different media types such as UTP and fiber optical.
To connect two different network architectures such as token ring and Ethernet.
To connect LAN network with Telco company’s office (Known as DTE device).
To access DSL services (known as DSL Router).

## Slide 21: Brouter
Brouters are the combination of router and bridge.

## Slide 22: Gateway
Gateway is used to forward the packets which are intended for remote network from local network. A default gateway address is the address of gateway device. If packet does not find its destination address in local network then it would take the help of gateway device to find the destination address in remote network. A gateway device knows the path of remote destination address
Examples of Gateway
Email Gateway :- Translate SMTP e-mail in standard X.400 format before forwarding.
GSNW Gateway :- Allow windows clients to access resources from NetWare server.
PAD Gateway :- Provides connectivity between LAN network and X.25 network.

## Slide 23: Proxy
Proxy can be a dedicate device or software. Proxy is used to hide the internal network from external world. All communication will go through the proxy. External computer will be able to access only proxy. Thus Proxy makes tampering with an internal system from the external network more difficult.

## Slide 24: THANK YOU